Scaling up:
Making point-source multichannel content work for large listening areas
A project report from previous VDT International Conventions
Jörn Nettingsmeier (VDT) <nettingsmeier@tonmeister.de>
Peter Maier (concept A acoustics GmbH) <peter.maier@concept-a.net>

---
First problem: tone colour
- Perceived tone-colour is a mix of:
direct sound, on axis - easy, near-perfect for quality speakers

---
First problem: tone colour
- Perceived tone-colour is a mix of:
1. direct sound, on axis - easy, near-perfect for quality speakers
2. direct sound, off axis - harder, requires controlled radiation
              1. (We can EQ one or the other, but not both.)

---
First problem: tone colour
- Perceived tone-colour is a mix of:
1. direct sound, on axis - easy, near-perfect for quality speakers
2. direct sound, off axis - harder, requires controlled radiation
              1. (We can EQ one or the other, but not both.)
3. reverberant sound - depends on room and speaker patterns,
       usually strong coloration
              1. (We cannot EQ this independent of the direct sound.)

---
First problem: tone colour
- Speakers do not radiate uniformly.
- Low frequencies are emitted in all directions.
- Directivity increases with frequency.
- Nominal coverage is usually reached at 1 kHz.
- Coverage in the treble range is narrower.
- → The diffuse field can become bass-heavy.
- → Bass buildup gets worse the more speakers are used.

---
First problem: tone colour
- Speakers do not radiate uniformly.
- Low frequencies are emitted in all directions.
- Directivity increases with frequency.
- Nominal coverage is usually reached at 1 kHz.
- Coverage in the treble range is narrower.
- → The diffuse field can become bass-heavy.
- → Bass buildup gets worse the more speakers are used.
- In a reverberant room, wide-dispersion speakers might lead to a more natural tone color, even though they excite the room more.

---
First problem: tone colour
Typical rooms have very non-uniform decay:

---
First problem: tone colour
Typical rooms have very non-uniform decay:

---
First problem: tone colour
Typical rooms have very non-uniform decay:
Pronounced ringing below the
Schroeder frequency: the room acts
as a resonator.

---
First problem: tone colour
Typical rooms have very non-uniform decay:
Pronounced ringing below the
Schroeder frequency: the room acts
as a resonator.
Strong coloration of the reverberant
field due to uneven decay.

---
First problem: tone colour
Typical rooms have very non-uniform decay:
This is why reverberation must not be reduced to a single value!
Pronounced ringing below the
Schroeder frequency: the room acts
as a resonator.
Strong coloration of the reverberant
field due to uneven decay.

---
Second problem: clarity
- Clarity is defined as
  - the ratio of initial sound energy versus remaining sound energy,
    that is, the „early sound“ versus the late reverberation.
C50 = int from{0} to {50ms} p²(t) / int from{50ms} to {inf} p²(t)
Clarity is an indicator for speech intelligibility, musical precision, directness, and hence emotional „impact“.

---
Second problem: clarity
Clarity is defined as
C50 = int from{0} to {50ms} p²(t) / int from{50ms} to {inf} p²(t)
t
t0: 50 or 80 ms
C50 (speech)
C80 (music)

---
Room treatment
- Tone colour and clarity are determined by the diffuse sound field.
- The only way to correct that is room treatment.
- A good starting point is a measurement of the room's decay properties.

---
Room treatment
- This is the T30 of room R3 at Tonmeistertagung 2012,
  empty and untreated.

---
Room treatment

---
Room treatment
- three layers of stage cloth
- wideband absorbers along room edges
- wideband absorbers in corners

---
Room treatment
- This is room R3 after treatment.
- We are within the limits of EBU Tech 3276 (recommendation for control room acoustics), extrapolated for room size.

---
Electronic correction
- After room treatment, consider EQ:
- → notch remaining room modes
- → low-shelf bass buildup
- → fine-tune subjective tone color
- When measuring the room frequency response, look at longer integration windows (up to the reverberation time).

---
Third problem: stereophonic localisation
- Stereophonic localisation cues:
- inter-aural level difference (ILD)
- inter-aural time difference (ITD)
- Working ranges:
- ΔL:	0 .. 18 dB
- Δt:	0 .. 1.5 ms
- (illustration and table by
  Eberhard Sengpiel)

---
Third problem: stereophonic localisation
- A 10 x 15 m auditorium, with stereo loudspeakers spaced 8 m apart (black dots at bottom).
- Green areas denote less than 50% ITD localisation error.
- In red areas, ITD imaging collapses to nearest speaker.
- In blue areas, spill from opposite speaker may reach the echo threshold.

---
Third problem: stereophonic localisation
- ILD cues are more robust in comparison.
- Green area denotes less than 50% ILD localisation error.
- The red areas where the image collapses into the nearest speaker are much smaller.

---
Third problem: stereophonic localisation
Area of satisfactory
localisation for
AB stereo (spaced omnis)

---
Third problem: stereophonic localisation
Area of satisfactory
localisation for XY stereo
(coincident directional mics)

---
Third problem: stereophonic localisation

---
Third problem: stereophonic localisation
- Stereo localisation does not scale.
- Different stereo techniques exhibit wildly different localisation behaviour.
- The only way to handle it is to communicate the limitations to presenters and audience.

---
Third problem: stereophonic localisation
- With an added center speaker (and a suitable signal set), scalability improves dramatically:
- The frontal stereo bases are only half as wide. We have perfect center stability.
- Moving to 5.1, the challenge is to balance front and rear speakers.
- The rears must be loud enough to provide satisfactory envelopment, and not too loud to not disturb the frontal image. The tolerance range is often less than 3 dB.

---
Level balance in surround systems
- move the speakers as far away from the audience as possible, EQ for boundary effects
- - define a golden seat A, arrange L, C, R, Ls, and Rs angles according to ITU BS R-775 and calibrate for equal loudness and arrival time in A
- - define the golden seat among the cheap seats B, measure and average L,C, and R level and arrival times
- - calibrate additional surrounds Ls2 and Rs2 for correct arrival time and level in B

---
Level balance in surround systems
Consider the spill from the rear surrounds into the golden seat A:
- It will be late, and lower in level:
- This is no worse than normal room effects. The key factor is to arrive at a spill delay that is long enough to not comb too much, and short enough to not cause an echo.

---
Demo
- Short demo/workshop at Theater im Palais
  (the building opposite the MUMUTH entrance)
  at 1:50 pm.
- Thanks for your attention.
- Any questions?

---
Listening examples:
- Tom Ammermann, Blug plays Hendrix: Little Wing. 5.1
- Günther Wollersheim, Anton Bruckner: 5th Symphony (Köln Philharmonic). 5.1
  Julien Herion, Stadtklang. 5.1
- Julian Klapp, Steve Reich: Six Marimbas (Johannes Wippermann), 5.1
- selected from the VDT Award winners („Goldener Bobby“) 2012